| Student: | Test |
| --- | --- |
| Date: 2 May 2004 |  |
| Questions: |  |
| Design Requirements (6 marks) Explain the requirements for materials for reactor coolant and moderator, list the usual materials and discuss how they meet the requirements. (50%) Explain how the type of the reactor influences the selection of the moderator and coolant material. (50%) Power Reactor Types (6 marks) For the reactor shown in the figure below explain: Draw a primary coolant flow diagram and explain the flow path. (30%) Explain the configuration of the core and fuel assemblies. (30%) List the most important difference compared to a CANDU reactor. (40%) Process Design Evolution (5 marks) Explain the main direction in CANDU process design evolution. (50%) Capture the most important changes to the ACR-700 design as compared to the traditional CANDU. (50%) |

Flow Instabilities (5 marks) For the flow instability diagram shown in the figure below: Explain the instability criterion. (30%) Discuss the effect of channel heat transfer to the instability curve. (30%) Discuss the importance in case of flow diversion in a loop with two parallel non-equal channels. (40%) Thermal Efficiency (6 marks) Define the thermal efficiency of a NPP and explain the factors of influence. (50%) Explain the methods (design options) to increase NPP thermal efficiency, and discuss feasibility and importance of each option. (50%) Steam Generator Calculations (6 marks) Explain the principles of the design of the steam generator (40%) Explain the behavior of the steam generator using the heat duty diagram (60%) Fuel-Coolant Heat Transfer (6 marks) Draw a diagram of temperature distribution across the fuel element and coolant in radial direction, and explain the change of rate of heat transfer across different components (50%) Draw a diagram of temperature distribution along the fuel element and coolant in axial direction and explain the change of rate of heat transfer along different components (50%)

Two-phase Flow (5 marks) Identify all boiling heat-transfer modes and transition points in the boiling curve. (40%) State all possible boiling heat-transfer modes encountered in a heat-flux-controlled system with increasing heat flux from single-phase liquid flow at the same local flow conditions (i.e., pressure, mass flux and quality). (25%) State all possible boiling heat-transfer modes encountered in a temperature-controlled system with increasing wall temperature from single-phase liquid flow at the same local flow conditions (i.e., pressure, mass flux and quality). (35%) Film Boiling (5 marks) Identify heat-transfer modes (i.e., conduction, convection, and radiation) between the heated wall and two phases in dispersed-flow film boiling. (40%) Provide the direction of heat flow at each solid line. (20%) What does the dashed line represent? (40%)

Pressure Drop (7 marks) Identify all pressure-drop components with flow over a string of heated 37-element bundles inside a horizontal pressure tube. (20%) Arrange thermodynamic qualities for the following transition points in ascending order: (20%) Onset of annular flow Onset of nucleate boiling Onset of significant void Saturation liquid point Saturation vapour point Calculate the two-phase pressure drop for light-water flow over the 37-element bundle (element outside diameter of 13.06 mm) inside a pressure tube (inside diameter of 103.86 mm) (60%) Pressure: 9 MPa Mass flow rate: 17 kg/s Mass quality: 0.2 Flow area: 3515 mm2 Bundle loss coefficient: 1.7 Saturated liquid density: 704.7 kg/m3 Saturated vapour density: 48.8 kg/m3 Two-phase multiplier, 2LO = (1 + x (f / g - 1))

CHF (7 marks) Evaluate the critical heat flux, using the attached CHF table, for the 37-element bundle (element outside diameter of 13.06 mm) inside a pressure tube (inside diameter of 103.86 mm) at the pressure of 9.5 MPa, mass flow rate of 17 kg/s and thermodynamic quality of 20%. (50%) Evaluate the critical heat flux for the bundle inside a pressure tube with 5% diametral creep (i.e., pressure-tube inside diameter is 5% larger) at the same flow conditions. (25%) Identify the boiling heat-transfer modes for these two cases if the local heat flux is 1500 kW/m2. (25%) Pressure (kPa) Mass Flux (kg.m-2.s-1) Quality _0.5 _0.4 _0.3 _0.2 _0.15 _0.1 _0.05 0 0.05 0.1 0.15 0.2 0.25 0.3 0.35 0.4 0.45 0.5 0.6 0.7 0.8 0.9 1 9000 0 4836 4571 4301 4034 3902 3783 3639 3352 2503 1977 1637 1290 1179 992 843 739 660 608 560 471 431 349 0 9000 50 5422 5114 4813 4547 4432 4335 4213 3960 3071 2528 2304 2110 1945 1810 1699 1610 1536 1457 1152 971 938 650 0 9000 100 5916 5571 5251 4988 4892 4811 4704 4462 3658 3134 2976 2841 2697 2575 2458 2373 2317 2165 1554 1306 1300 1040 0 9000 300 6366 5916 5527 5300 5260 5239 5236 5194 4944 4270 3692 3478 3344 3257 3065 2894 2713 2334 1672 1380 1197 899 0 9000 500 6641 6100 5668 5412 5332 5205 5147 5114 4925 4243 3625 3364 3160 2999 2887 2741 2351 1983 1583 1282 904 626 0 9000 1000 7221 6432 5947 5625 5398 4936 4705 4703 4697 4204 3520 3118 2854 2661 2545 2118 1553 1143 984 729 346 311 0 9000 1500 7976 7023 6356 5856 5535 4958 4693 4467 4189 3730 3227 2850 2712 2495 2034 1429 1081 892 546 350 131 119 0 9000 2000 9111 8171 7160 6258 5863 5299 4835 4196 3569 3097 2746 2448 2312 1931 1428 1027 745 603 345 186 97 48 0 9000 2500 10108 9252 8185 7162 6749 6025 5004 4119 3339 2797 2521 2241 1942 1373 1028 809 570 348 211 136 96 48 0 9000 3000 10887 10041 8998 7755 7210 6399 5097 4045 3240 2604 2289 2038 1724 1354 967 708 508 393 282 169 103 49 0 9000 3500 11622 10683 9660 8227 7395 6453 5140 3995 3155 2487 2124 1896 1643 1276 952 650 457 419 305 184 107 54 0 9000 4000 12336 11283 10200 8756 7669 6674 5266 3983 3066 2349 1931 1750 1604 1375 982 664 558 499 331 190 108 55 0 9000 4500 13022 11857 10680 9235 7924 6936 5469 4047 3026 2245 1827 1719 1631 1385 1037 771 670 615 381 205 109 56 0 9000 5000 13683 12418 11127 9685 8259 7305 5645 4183 3080 2249 1836 1755 1663 1416 1152 908 816 717 445 239 116 57 0 9000 5500 14332 12927 11580 10180 8872 7818 5764 4272 3210 2355 1963 1856 1760 1542 1290 1071 935 801 512 281 130 62 0 9000 6000 14961 13402 11998 10758 9759 8777 6149 4331 3303 2421 2126 2045 1937 1699 1500 1219 1072 892 578 329 157 73 0 9000 6500 15570 13909 12387 11336 10230 9257 6353 4416 3344 2492 2346 2317 2197 1985 1710 1431 1170 977 646 378 186 88 0 9000 7000 16165 14403 12779 11578 10702 9737 6355 4542 3482 2788 2527 2402 2245 2070 1785 1497 1258 1058 712 426 216 103 0 9000 7500 16748 14881 13166 11824 10747 9739 6394 4637 3660 3076 2877 2745 2567 2142 1800 1557 1339 1140 778 475 248 118 0 9000 8000 17323 15340 13551 12107 10954 9741 6556 4714 3838 3419 3342 3299 3162 2736 2042 1620 1420 1218 842 525 281 134 0 10000 0 4568 4337 4103 3874 3760 3658 3534 3274 2464 1922 1596 1276 1163 991 849 748 680 625 562 474 410 282 0 10000 50 5126 4857 4591 4336 4230 4146 4040 3814 3002 2482 2256 2057 1890 1750 1641 1555 1482 1415 1139 965 886 645 0 10000 100 5597 5296 5007 4734 4637 4565 4472 4253 3512 3015 2865 2728 2582 2457 2347 2266 2213 2105 1551 1296 1211 897 0 10000 300 6039 5642 5266 4961 4891 4870 4868 4832 4636 4016 3506 3393 3315 3233 2987 2781 2593 2240 1383 1076 1021 674 0 10000 500 6318 5831 5417 5074 4965 4855 4800 4765 4599 4013 3353 3165 3038 2871 2644 2239 2002 1651 1137 848 796 522 0 10000 1000 6912 6184 5732 5328 5073 4676 4463 4376 4328 3822 3225 2936 2680 2484 2171 1342 1033 802 636 460 298 250 0 10000 1500 7650 6747 6118 5570 5212 4712 4476 4178 3843 3402 2958 2559 2393 2102 1655 938 647 547 451 253 127 86 0 10000 2000 8720 7826 6896 6030 5591 5000 4575 3974 3349 2872 2468 2106 1912 1402 972 677 480 355 303 155 95 46 0 10000 2500 9664 8829 7895 7010 6589 5726 4678 3901 3191 2623 2258 1901 1601 1035 666 533 399 280 195 126 95 47 0 10000 3000 10400 9580 8648 7587 7077 6149 4779 3891 3089 2444 2030 1701 1419 1001 647 478 388 300 256 147 97 48 0 10000 3500 11099 10200 9259 8008 7253 6254 4797 3830 3005 2327 1877 1591 1361 1062 723 525 414 364 274 151 99 51 0 10000 4000 11783 10775 9774 8533 7582 6503 4841 3728 2909 2178 1686 1470 1345 1147 870 641 492 429 291 160 101 53 0 10000 4500 12444 11327 10230 8989 7824 6787 4940 3754 2892 2087 1605 1476 1410 1262 1016 768 590 545 359 188 105 54 0 10000 5000 13081 11867 10655 9402 8114 7092 5116 3898 2977 2088 1612 1562 1539 1383 1130 876 686 639 430 229 112 56 0 10000 5500 13694 12355 11078 9834 8616 7476 5265 4034 3114 2208 1742 1692 1663 1496 1261 993 796 703 490 274 126 59 0 10000 6000 14268 12772 11467 10320 9342 8224 5687 4147 3227 2286 1927 1902 1821 1641 1440 1183 993 842 553 317 150 70 0 10000 6500 14835 13236 11837 10808 9713 8600 5912 4241 3275 2378 2206 2200 2098 1895 1687 1382 1133 942 620 363 179 85 0 10000 7000 15399 13708 12204 11028 10083 8975 5926 4267 3390 2707 2422 2309 2182 2003 1720 1432 1212 1021 686 410 208 99 0 10000 7500 15952 14166 12567 11253 10103 8977 5940 4279 3559 2995 2729 2594 2483 2092 1733 1484 1287 1097 750 459 240 114 0 10000 8000 16496 14588 12938 11536 10351 8979 5955 4484 3783 3325 3120 2988 2864 2621 2015 1596 1393 1182 812 507 272 129 0

Basic Conservation Equations for Two-Fluid Models (6 marks) Write the microscopic and macroscopic form of the conservation equations and explain the role of each term. CATHENA Computer Code (6 marks) Explain the most important features of the CATHENA thermal-hydraulic model (model characteristics, conservation equations, flow regime map, nodalization, which parameters are calculated, etc.) (50%) Explain the most important features of the CATHENA heat transfer model (which models are available, which parameters are calculated, linkage to hydraulics, correlations etc.) (50%) Thermal-hydraulic Network Calculations (6 marks) Explain the advantages and disadvantages of different numerical schemes: explicit, semi-implicit (implicit in flow and pressure, explicit in mass and enthalpy), and fully implicit. Nodalization (6 marks) Write the mass equations for the thermal-hydraulic system below and show it in matrix form. Bonus for high mark: Write the momentum equations for the thermal-hydraulic system above and show it in matrix form.